## Slide 1: Federal Transmission Policies for a Clean Energy Grid NASUCA June, 2021
Rob Gramlich
www.gridstrategiesllc.com
@RobGramlichDC

## Slide 2: Interregional Transmission Keeps the Lights On in Winter Storm Uri Feb 2021 MISO imported 13 GW, ERCOT only 0.8 GW (East to West flow) Eastern polar vortex incidents in 2014, 2018 served by Midwest power (West to East flow) For transmission planning and cost allocation—who is the beneficiary???

## Slide 3: Low-cost decarbonization requires large scale transmission 10s of GWs of power transfer back and forth across and between regions 2-3x increase in national transmission capacity
https://www.cell.com/joule/fulltext/S2542-4351(20)30557-2
https://cleanenergygrid.org/wp-content/uploads/2020/11/Macro-Grids-in-the-Mainstream-1.pdf
Modeled flows NREL Seam study

## Slide 4: Bigger is lower cost in transmission
765kv lines have ~1/6 the losses as 345 kV
Bigger lines
Lower $/MW-mile

## Slide 5: ~800 GW of clean energy stuck in interconnection queues Planning a HV network through an interconnection process costs more than regional planning
Projects Entering
Queues
Completed
Projects
More recent
Higher cost

## Slide 6: First, get the most out of the existing grid with Grid-Enhancing Technologies (GETs) See www.watt-transmission.org
GET some Dynamic Line Ratings, topology optimization, storage-as-transmission, power flow control
GETs are
  VERY low cost, $0.5m - $25m
  deployable in MONTHS
  scalable
  modular
  mobile and re-deployable
FERC shared savings incentive conference September 2021

## Slide 7: Big transmission CAN be built! Recent US Large-Scale Expansions
MISO MVP, SPP priority projects, ERCOT CREZ
3:1 Benefit-Cost ratios
Winning formula:
  Pro-active multi-benefit planning
  Broad, beneficiary pays cost allocation

## Slide 8: FERC Initiatives For low delivered cost energy (generation + transmission)
4. Transmission planning and cost allocation
  Estimate generation as well as load
  Multi-benefit, de-silo—congestion, resilience, public policy
  Resilience scenarios that might afflict a given region
  Electrification estimates in load forecasts
  Benefit-cost analysis
  Inter-regional
Kill MOPR
Interconnection reforms
Grid-Enhancing Technologies incentives
Encourage markets and RTOs
Chairman Glick: revisiting the planning process for developing high-voltage power lines across the country should be “front and center” at the Commission. “That’s my goal: to have something in place at least to start the process, whether it’s rulemaking or a policy approach, before the end of the summer.”

## Slide 9: Transmission Policy in the 117th Congress
Infrastructure legislation:
  Transmission Investment Tax Credit
  Funding for large scale transmission
  Anchor tenant loans
  Power Marketing Administration loan authority
  DOE studies and helping with planning
Direct FERC to fix interregional planning and cost allocation
Funding for states to constructively engage in transmission planning
Consider transmission siting

## Slide 10: Executive Agency Transmission Initiatives Sec. Granholm: “deploy, deploy, deploy”
Improve federal permitting
  DOT: highways
  DOI: federal lands
Federal backstop siting
  DOE and FERC
Grid Deployment Authority
WAPA Transmission Infrastructure Program loans
Loan guarantees—DOE Loan Program Office