## Slide 1: DER Integration into Wholesale Markets
3rdRail Inc. and Berkeley Lab Affiliate
Training Webinar for National Association of State Utility Consumer Advocates
June 29, 2022
This presentation was funded by the U.S. Department of Energy’s Grid Modernization Laboratory Consortium.
Fredrich Kahrl

## Slide 2: Overview
Background: Distributed energy resource (DER) integration into wholesale markets
Barriers to DER integration
Nearer-term priorities for DER integration
Longer-term priorities for DER integration
Key considerations for public utility commissions
Questions public utility commissions can ask

## Slide 3: Background: What is DER integration and why is it important? (1)
“DER integration” refers to the integration of DER into distribution system operations and wholesale markets and operations, enabling closer coordination between distribution (D) and transmission (T) system planning and operations.
Better T-D coordination will reduce required electricity system investment and operating costs.
DER integration covers a wide range of areas: DER interconnection, T&D planning, data access and communication, distribution system operations, utility regulation and tariffs, and wholesale markets.
Transmission (ISO-NE)
Distribution Utility C
Transmission (NYISO)
NYISO has a generator outage and low wind, leading to high energy prices
ISO-NE has a cloudy day with limited solar generation, leading to high energy prices
Distribution customers with storage shift discharging to system peak hours, and customers with responsive load reduce output (e.g., EVs charge as little as possible).
Coordinated T-D operations example
Distribution
Utility B
Distribution
Utility A

## Slide 4: Background: What is DER integration and why is it important? (2)
NYISO relies more on imports from ISO-NE to meet resource adequacy (RA) needs
ISO-NE reduces total RA need and T investments
Distribution customers invest in a significant amount of distributed generation, distributed storage, and load management that is coincident with ISO-NE and NYISO peak demands.
Transmission (ISO-NE)
Distribution Utility C
Transmission (NYISO)
Coordinated T-D operations example
Distribution
Utility B
Distribution
Utility A

## Slide 5: Background: Storage placement illustrates why DER integration is important
Better coordination between D and T systems can resolve the question of how much storage should be optimally located in different parts of the electric grid, based on where it has the most value for the lowest cost.
From a regulator’s perspective, it’s important to think about “value and cost to whom”?

## Slide 6: Background: Approaches to DER participation in wholesale markets
Under FERC Order 2222, DER can participate on the supply side individually or through aggregation by making offers directly into ISO markets.
  ISO directly settles with DER owner or aggregator
DER can also participate in ISO markets on the demand side through LSE demand bids or metered demand.
  ISO settles with LSE, DER offsets LSE ISO charges, and LSE settles with DER owner or aggregator.
DER
Supply-side offers
Demand-side bids (day-ahead market) and metered demand (real-time market)
DER aggregator
ISO
Generator
Competitive LSE
Utility LSE
DER
DER

## Slide 7: Key elements in DER integration
Distribution Interconnection
Utility assesses DER impacts on D system, determines whether D upgrades will be needed
Distribution Planning
Utility pre-emptively builds D infrastructure, determines upgrades that will be triggered through interconnection and how DER will be operated
Distribution Operations and Markets
Utility ensures D reliability, may operate DER to avoid reliability violations (and in the future potentially to minimize D costs subject to D security constraints)
Wholesale Markets
ISO ensures T reliability, operates markets for RA, day-ahead/real-time energy and ancillary services
Utility Regulation and Tariffs
State regulators determine utility incentive framework and approve tariffs and rates

## Slide 8: Barriers to DER integration (1)
DER interconnection
  Interconnection standards – Many states have yet to adopt and implement IEEE 1547-2018 (focused on smart inverters and voltage support).
  Process enhancement and standardization – Coordination among states is limited in terms of distribution interconnection enhancements (timelines, technical requirements, upgrade cost allocation).
  Interconnection costs – Cost allocation methods are in flux. States are still at an early stage in allowing DER to avoid D upgrades in exchange for limiting generation or being curtailed in some hours (“flexible interconnection”).
Distribution planning
  T-D planning coordination – D utilities and ISOs have limited coordination on load/DER forecasts and engineering studies.
  Regional resource planning coordination – Coordination is limited among ISOs, state PUCs and energy offices, utilities, generators, and DER developers on scenarios for regional resource development.

## Slide 9: Barriers to DER integration (2)
Distribution operations
  DER overrides – Most utilities do not yet have processes for overriding ISO dispatch of DER aggregators, including outage communication capabilities.
  DSO functionality and grid investments – There is a lack of clarity over future monitoring, communications, and dispatch/control needs and investment requirements.
Utility regulation and tariffs
  Utility incentives – Utilities may not have incentives to maximize the value of DER.
  DER tariffs – Many utilities do not have time-varying, market-based tariffs for customers that can shift load and have behind-the-meter generation.
Wholesale markets
  Demand participation – Opportunities for intraday participation in ISO markets through demand bids are limited.
State-federal jurisdiction
  Overlapping jurisdiction – Federal-state jurisdiction over distribution interconnection, planning, operations, and markets remains unclear in some cases.

## Slide 10: Nearer-term priorities
DER interconnection
  Adopting and implementing IEEE 1547-2018
  Investing in interconnection process improvements, with some amount of regional or national standardization
  Allowing static export limits for distributed generation paired with storage*
Distribution planning
  Coordinating DER/load forecasting for T-D systems; undertaking “what if” regional resource scenario analysis through regional fora
DER operations
  Developing transparent, non-discriminatory approaches to DER overrides that can evolve into more active distribution operations over time
  Beginning to consider future models for distribution system operations and mapping out needed investments over time
Utility regulation and tariffs
  Exploring incremental improvements to utility performance incentives and time-of-use-based tariffs for DER customers
State-federal jurisdiction
  Establishing a FERC-state working group on distribution jurisdiction
* See, for instance, Use of Operating Agreements and Energy Storage to Reduce Photovoltaic Interconnection Costs, https://eta-publications.lbl.gov/sites/default/files/80556.pdf

## Slide 11: Longer-term priorities
DER interconnection
  Implementing more flexible approaches to interconnection of DER and EV loads, eventually allowing dynamic curtailment (dispatch) of DER
Distribution planning
  Developing new planning criteria for D investments (e.g., moving toward a reliability, economic, policy framework like the T system)
DER operations
  Right-sizing the sophistication of utility distribution operations (e.g., how actively do DSOs need to manage D systems?)
Utility regulation and tariffs
  Creating open access rules for the distribution system
  Developing multi-part tariffs for DER customers, with more sophisticated time-varying distribution rates
  Developing future utility business models (e.g., balancing cost recovery and economic bypass of grid charges)
Wholesale markets
  Allowing intraday demand bids and locational marginal pricing settlement for loads

## Slide 12: Key considerations for public utility commissions
Starting from fundamentals – Taking a bottom-up approach to problem solving, being clear about terms and concepts (e.g., be careful with the term “DER”), and developing a working framework of options for future distribution operations and markets
Focusing on least-regrets – In the near term, focusing resources on incremental, least-regrets changes that build on existing institutions
Keeping a long-term perspective – Starting to think about solutions to longer-term challenges, creating a vision for future distribution system operations and markets, and developing a long-term plan that prioritizes areas to tackle over time
Working together – Participating in regional/national fora and learning from other jurisdictions

## Slide 13: Questions state utility consumer advocates can ask
Where are nearer-term gaps in current distribution interconnection, distribution planning and T-D planning coordination, distribution operations, and utility DER tariffs?
How can nearer-term gaps be most effectively and efficiently addressed, while laying the foundations for a transition to future distribution system operations and markets?
What is the longer-term vision for future distribution system operations and the role (and business model) of the distribution utility?
Where would clearer state-federal jurisdiction be most helpful in the nearer and longer term?
Where are opportunities for public utility commissions to work together on DER integration, and what balance between regional (e.g., NECPUC) or national (e.g., via NARUC) fora would provide the most helpful venue for collaboration?

## Slide 14: Resources for more information
Energy Systems Integration Group (ESIG), 2022, DER Integration into Wholesale Markets and Operations, https://www.esig.energy/wp-content/uploads/2022/01/ESIG-DER-Integration-Wholesale-Markets-2022.pdf
Advanced Energy Economy (AEE) and GridLab, 2022, Removing Barriers to DER Participation in Wholesale Markets, https://gridlab.org/wp-content/uploads/2022/01/eLab-Accelerator-DER-Wholesale-Markets.pdf
Advanced Energy Economy (AEE) and GridLab, 2022, FERC Order 2222 Implementation: Preparing the Distribution System for DER Participation in Wholesale Markets, https://gridlab.org/wp-content/uploads/2022/01/AEE-GridLab-FERC-O.2222-Campaign-Final-Report.pdf

## Slide 15: Contact
Fritz Kahrl
3rdRail Inc.
fkahrl@outlook.com
Lisa Schwartz
Lawrence Berkeley National Laboratory
lcschwartz@lbl.gov