## Slide 1
A Snapshot of EV-Specific Rate Designs Among U.S. Investor-Owned Electric Utilities
Peter Cappers, Andrew Satchwell (Berkeley Lab)
Cameron Brooks, Sam Kozel (E9 Insight)
May 11, 2023
This work was funded by the U.S. Department of Energy’s Office of Electricity under Contract No. DE-AC02-05CH11231.

## Slide 2: How are EV-Specific Electric Utility Rates Designed Presently?
Objective
Provide regulators, utilities, and the EV industry with a more robust understanding of how EV-specific electric utility rates could be designed and how they are actually being designed presently in the United States
Caveat
Focused on IOUs, excluded energy marketers, municipal utilities, and cooperative utilities
Did not assess customer enrollment or response to EV-specific rate designs
Methods
Develop a framework for identifying the design elements of EV-specific rates
Collect electric utility tariff filings with state utility regulators of EV-specific rates
Apply the framework to the tariff filings to develop a database that categorizes EV-specific rates
Evaluate the database to characterize the landscape of EV-specific rate designs

## Slide 3: Retail Rates are Designed Based on Two (2) Broad Concepts
Recover a utility’s costs (i.e., revenue requirement), apply sound ratemaking principles; and are considered just and reasonable
Satisfy certain policy and/or market objectives that can vary based on a state’s distinct rules, regulations, and policies, as well as different stakeholder motivations

## Slide 4: Five (5) Policy-Driven Objectives Potentially Used as the Basis for EV-Specific Rate Designs
Promote EV adoption
Grid management
System economic efficiency
Decarbonization
Equity
Recover a utility’s costs (i.e., revenue requirement), apply sound ratemaking principles; and are considered just and reasonable
Satisfy certain policy and/or market objectives that can vary based on a state’s distinct rules, regulations, and policies, as well as different stakeholder motivations

## Slide 5: Five (5) Policy-Driven Objectives Used as the Basis for EV-Specific Rate Designs
Promote EV adoption
Grid management
System economic efficiency
Decarbonization
Equity
Recover a utility’s costs (i.e., revenue requirement), apply sound ratemaking principles; and are considered just and reasonable
Satisfy certain policy and/or market objectives that can vary based on a state’s distinct rules, regulations, and policies, as well as different stakeholder motivations

## Slide 6: Five (5) Policy-Driven Objectives Used as the Basis for EV-Specific Rate Designs
Promote EV adoption
Grid management
System economic efficiency
Decarbonization
Equity
Recover a utility’s costs (i.e., revenue requirement), apply sound ratemaking principles; and are considered just and reasonable
Satisfy certain policy and/or market objectives that can vary based on a state’s distinct rules, regulations, and policies, as well as different stakeholder motivations

## Slide 7: Five (5) Policy-Driven Objectives Used as the Basis for EV-Specific Rate Designs
Promote EV adoption
Grid management
System economic efficiency
Decarbonization
Equity
Recover a utility’s costs (i.e., revenue requirement), apply sound ratemaking principles; and are considered just and reasonable
Satisfy certain policy and/or market objectives that can vary based on a state’s distinct rules, regulations, and policies, as well as different stakeholder motivations

## Slide 8: Five (5) Policy-Driven Objectives Used as the Basis for EV-Specific Rate Designs
Promote EV adoption
Grid management
System economic efficiency
Decarbonization
Equity
Recover a utility’s costs (i.e., revenue requirement), apply sound ratemaking principles; and are considered just and reasonable
Satisfy certain policy and/or market objectives that can vary based on a state’s distinct rules, regulations, and policies, as well as different stakeholder motivations

## Slide 9: EV rate design typically comprised of five (5) different components
EV Rate Design
Metering Configurations
Temporal Differentiation
Locational Differentiation
Demand Charges
Charging Controls
Notes: .

## Slide 10: Metering Configurations
Whole home/facility consumption via account meter
EV charging consumption
via account meter
Submetering via EVSE or vehicle

## Slide 11: Temporal Differentiation of Volumetric Energy Charge
Chart: August Day
 | 28286 | 27023 | 26150 | 25830 | 26229 | 27530 | 29470 | 30667 | 31753 | 32861 | 33234 | 33075 | 33400 | 34294 | 35778 | 37735 | 39527 | 40732 | 40914 | 40384 | 39751 | 37775 | 34643 | 31948
Chart: 
| 0.70833333333333337 | 0.71180555555555547 | 0.71527777777777779 | 0.71875 | 0.72222222222222221 | 0.72569444444444453 | 0.72916666666666663 | 0.73263888888888884 | 0.73611111111111116 | 0.73958333333333337 | 0.74305555555555547 | 0.74652777777777779 | 0.75 | 0.75347222222222221 | 0.75694444444444453 | 0.76041666666666663 | 0.76388888888888884 | 0.76736111111111116 | 0.77083333333333337 | 0.77430555555555547 | 0.77777777777777779 | 0.78125 | 0.78472222222222221 | 0.78819444444444453 | 0.79166666666666663 | 0.79513888888888884 | 0.79861111111111116 | 0.80208333333333337 | 0.80555555555555547 | 0.80902777777777779 | 0.8125 | 0.81597222222222221 | 0.81944444444444453 | 0.82291666666666663 | 0.82638888888888884 | 0.82986111111111116 | 0.83333333333333337 | 0.83680555555555547 | 0.84027777777777779 | 0.84375 | 0.84722222222222221 | 0.85069444444444453 | 0.85416666666666663 | 0.85763888888888884 | 0.86111111111111116 | 0.86458333333333337 | 0.86805555555555547 | 0.87152777777777779 | 0.875 | 0.87847222222222221 | 0.88194444444444453 | 0.88541666666666663 | 0.88888888888888884 | 0.89236111111111116 | 0.89583333333333337 | 0.89930555555555547 | 0.90277777777777779 | 0.90625 | 0.90972222222222221 | 0.91319444444444453
 | 32396 | 32328 | 32335 | 32462 | 32559 | 32697 | 32808 | 32922 | 33086 | 33115 | 33218 | 33283 | 33289 | 33126 | 33028 | 33069 | 33096 | 33088 | 33080 | 33092 | 33076 | 33096 | 33031 | 33016 | 32991 | 32913 | 32805 | 32757 | 32753 | 32711 | 32723 | 32729 | 32766 | 32782 | 32842 | 32847
Chart: Average Winter Day
 | 1047.0238 | 1015.5298 | 997.317 | 994.4449 | 1015.0327 | 1071.0134 | 1148.5729 | 1179.8973 | 1167.4092 | 1132.6815 | 1096.4762 | 1068.6548 | 1047.6994 | 1042.9628 | 1058.8304 | 1090.9911 | 1148.1324 | 1252.5342 | 1324.5238 | 1304.2545 | 1267.933 | 1220.8914 | 1154.2649 | 1087.9926
Chart: Average Summer Day
 | 1363.6263 | 1293.6237 | 1242.6384 | 1214.5995 | 1210.4113 | 1237.1909 | 1284.578 | 1332.2392 | 1390.8763 | 1427.7285 | 1465.0591 | 1514.8387 | 1574.0376 | 1654.7688 | 1745.2997 | 1831.2097 | 1897.3589 | 1934.9798 | 1924.0081 | 1867.9825 | 1810.3306 | 1716.0094 | 1582.5228 | 1452.9086
Seasonal Differentiation
Sub-hourly Differentiation
Hourly and Period Differentiation
Note that figures show temporal differentiation in load but there is also temporal differentiation in system costs and emissions that could be used as the design basis

## Slide 12: Locational Differentiation of Volumetric Energy Charge
Bulk power system
Distribution system
Site-specific

## Slide 13: Demand Charges
Seasonal or period-based charges
Timing of measured demand
Interval of measured demand
Demand ratchet

## Slide 14: Charging Controls
Utility system
Account meter
EV Supply Equipment (EVSE)
Electric Vehicle
Utility control via account meter or EVSE
Customer control via EVSE
One-way communication
Two-way communication

## Slide 15: Database of U.S. Electric Investor-Owned Utility EV-Specific Rates
Reviewed IOU tariff filings between 2012 and 2022
  Majority dated from 2018-2022
Eligible EV-specific rates:
  Required proof of EV ownership
  Designed for the purposes of reselling energy for use in EV charging
Identified 217 EV-specific rates from IOUs in 37 states and District of Columbia
  Offered (n=136): Rates that were either active or had been approved
  Proposed (n=12): Rates that had been filed but awaited a decision by the PUC
  Piloted (n=54): Rates that were temporary or where service was offered provisionally

## Slide 16: Currently Offered EV-Specific Rates are Almost Evenly Split Between Residential and Commercial Customers
Customer Class Categories
Fleet: Intended for specific use by public or private fleets (e.g., commercial fleets, school bus fleets)
Utility-owned: Intended for use at utility-owned charging equipment that is primarily deployed for public use, although examples at private multi-unit dwellings do exist
Mixed: Intended for use by both residential and commercial customers
Commercial: Intended for use by commercial, industrial, or general service classes of customers, as well as those who were not included in any other category
Residential: Intended for use by typical residential class customers, including multi-family

## Slide 17: Currently Offered EV Rates are Evenly Split Between Measuring Premise and EV Load w/ Utility Grade Meters
Meter Configuration Categories
Dedicated EV: The meter measured electricity consumption strictly for the EV
Whole Premise: The meter measured electricity consumption for the entire premise
  Utility Meter: An additional utility-grade meter was used to measure EV charging load
  Telematics: The EV’s own internal telematics were used to measure EV charging load
  EVSE: The EV supply equipment’s internal measurement capabilities were used to measure charging load

## Slide 18: Currently Offered EV Rates Overwhelmingly Include Period (TOU) and Seasonally Differentiated Designs
Temporal Differentiation Categories
Seasonal: Rate schedules that differed by season (e.g., summer and non-summer)
Period: Rate schedules that varied according to two or more multi-hour periods of the day (e.g., TOU rates)
Hourly: Rate schedules that varied according to the hour of the day (e.g., RTP)
Other: Rate schedules that varied temporally in any other way (e.g., as monthly load factors increase the cost per kWh charge decreases, critical peak energy charge overlay)

## Slide 19: No IOU Currently Offered a Locationally Differentiated EV-Specific Rate
Locational Differentiation Categories
Rate designs with locational differentiation can be as simple as volumetric energy charges that vary by location on the subtransmission (e.g., 34.5-69.0 kV) grid, or more complex differential coincident peak demand charges that are based on congestion of local distribution lines (e.g., below 34.5 kV).
For this analysis, rate levels reflective of cost differences at the bulk power system (e.g., above 69 kV) were not considered to have any locational differentiation.

## Slide 20: A Handful of Currently Offered EV Rates Included Traditionally or Alternatively Designed Demand Charges
Demand Charge Categories
Alternative Only: Rates that only included an alternative to a traditionally designed demand charge (e.g., demand subscription model, monthly upper limits on billed demand, level of demand charge tied to monthly load factor/station utilization)
Alternative Overlay: Rates that under particular conditions specified in the tariff overlaid an alternative to a traditional demand charge on top of a traditionally designed demand charge, both which were included in the tariff filing (e.g., discounted demand charge applied as a credit, reduced demand charge for off-peak usage, phasing out the $/kW demand charge in favor of a $/kWh volumetric energy charge based on station utilization)
Traditional Only: Rates that included a typical, traditional design for a demand charge
Holiday: Rates that included some version of a demand charge holiday, where the demand charge would be suspended for a period of time or where the holiday would otherwise be scheduled to sunset.

## Slide 21: Very Few Currently Offered EV-Specific Rates Explicitly Included Any Form of Charging Controls
Charging Control Categories
Utility Control Only: Rates that exclusively allow the utility to directly control the charging equipment, under specified circumstances, without the ability for a customer to override the utility control signals
Customer Override: Rates that give the customer the ability to override utility control signals, under specified circumstances
Customer Control Only: Rates that exclusively give the customer the ability to directly control charging equipment

## Slide 22: Dominant Offered EV-Specific Rate Designs Among U.S. IOUs
 | 1st Most Offered | 2nd Most Offered | 1st Most Offered | 2nd Most Offered | 1st Most Offered | 2nd Most Offered
Whole Premise Metering |  |  |  |  |  | 
Dedicated EV Metering |  |  |  |  |  | 
Flat or Block Energy Charge |  |  |  |  |  | 
TOU Energy Charge |  |  |  |  |  | 
Traditional Demand Charge |  |  |  |  |  | 
Alternative Demand Charge |  |  |  |  |  | 
Geographic Differentiation |  |  |  |  |  | 
Control Tech Requirement |  |  |  |  |  | 
Count / % of Class Total | 25 / 46% | 16 / 30% | 13 / 27% | 13 / 27% | 16 / 60% | 8 / 30%
Residential
Commercial
Utility-Owned

## Slide 23: Proposed and Piloted EV-Specific Rate Designs Were Generally Not All that Different From Offered Rates
The metering configurations, temporal differentiation, and locational differentiation observed in proposed and piloted rate designs were generally consistent with offered rates
  Commercial customer rate pilots generally included TOU rate designs with a handful testing different types of demand charge alternatives
  Residential customer rate pilots generally included TOU rate designs, but tested different ratios of peak to off-peak rate levels.
  Utility-owned charging station rate pilots commonly avoided the application of a demand charge and relied on volumetric energy rates set at a “competitive market” level
Limited degree of experimentation in more novel design elements was observed in a small number of pilots
  Handful of commercial rate pilots tested more granular temporal differentiation
  A few residential rate pilots tied the volumetric energy charges to different metering configurations

## Slide 24: Key Conclusions
Utilities and regulators may be highly motivated to currently promote EV adoption through simple rate designs while seeking broad management of grid impacts from the additional electric demand associated with charging loads (e.g., by encouraging off-peak charging)
The additional complexity introduced by alternatives to traditionally designed demand charges or outright holidays from them were deemed acceptable, by some, in order to support an industry at the beginning stages of a transition
The absence of highly dynamic temporal or locational rate designs suggests that, as in other utility applications, achieving the greatest level of economic efficiency is likely not as high a priority at the present time as other issues or may not be feasible or cost-effective due a variety of reasons (e.g., the existing metering infrastructure is too limited or nonexistent)
The general similarities between rates currently offered and those either proposed or piloted suggests limited interest in moving beyond the status quo in EV retail rate design

## Slide 25: Key Considerations for the Future
The implications of EV rate design objectives vis-à-vis other distributed energy resources (DERs) should be carefully considered, especially because states typically have different rate designs and policies/goals for different types of DERs (e.g., EV, PV)
Regulators and utilities should consider the frequency with which EV-specific rate designs are updated or altered to reflect changing grid, economic and/or environmental conditions as well as their effectiveness in achieving the stated (or, more likely, implicit) objective
Future research opportunities on EV-specific rates include:
  Assessing why particular rate design elements were proposed and approved, or why others were not
  Collecting and analyzing enrollment in and response to different rates offered at the same utility
  Understanding how recently enacted federal non-rate incentives are affecting rate design
  Identifying and categorizing utility EV program designs

## Slide 26: Questions/Comments

## Slide 27
Contact
  Peter Cappers | PACappers@lbl.gov
For more information
  Download publications from the Electricity Markets & Policy: https://emp.lbl.gov/publications
  Sign up for our email list: https://emp.lbl.gov/mailing-list
  Follow the Electricity Markets & Policy on Twitter: @BerkeleyLabEMP
  Access the report at https://emp.lbl.gov/publications/snapshot-ev-specific-rate-designs
Acknowledgements
  The work described in this study was conducted at Lawrence Berkeley National Laboratory and supported by the U.S. Department of Energy’s Office of Electricity under Contract No. DE-AC02-05CH11231. We would like to especially thank Chris Irwin (DOE) for his support of this work. For reviewing the study and providing valuable feedback, we thank Tanya Burns (Arara Blue Energy Group), Galen Barbose (Berkeley Lab), Garett Fitzgerald (SEPA), Michelle Levinson (World Resources Institute), Jeff Loiter (NARUC), Kara Podkaminer (DOE), and Melissa Whited (Synapse Energy)
  The views and opinions of authors expressed herein do not necessarily state or reflect those of the United States Government or any agency thereof, or The Regents of the University of California.