## Slide 1
Quantifying the Financial Impacts of Electric Vehicles on Utility Ratepayers and Shareholders
Andy Satchwell
with contributions from Juan Pablo Carvallo, Peter Cappers, James Milford, and Hadi Eshraghi
September 6, 2023 – NASUCA Webinar
This work was funded by the U.S. Department of Energy’s Office of Energy Efficiency and Renewable Energy Strategic Analysis Team under Contract No. DE-AC02-05CH11231.
Report and supplemental information available at: https://emp.lbl.gov/publications/quantifying-financial-impacts

## Slide 2: Policy and regulatory context – why does this matter?
Including customer EV adoption and balance among customers with and without EVs
Including how utility collects revenues and provides value to investors, as well as scope of utility roles and responsibilities
Ratepayer Impacts
Utility Shareholder Impacts

## Slide 3: Bookend charging strategies used in this study are characterized by system peak impacts
Low Peak Impact is the charging strategy that minimizes EV impacts on peak demand.
High Peak Impact is the charging strategy that maximizes EV impacts on peak demand.
The charging strategies adapt over time to achieve the performance objective.

## Slide 4: Summer-peaking, vertically integrated utility characterization
Chart: Annual utility costs (nominal $M)
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
Return on Rate Base Equity | 425.5401 | 455.2504 | 484.4925 | 513.3937 | 542.0829 | 570.6909 | 599.3508 | 628.1988 | 673.6108 | 702.7647 | 744.138 | 774.3286 | 805.4472 | 837.6574 | 871.1294 | 906.0407 | 942.5766 | 980.9311 | 1021.3075 | 1063.9193
Depreciation | 479.8177 | 516.6774 | 554.3023 | 592.8113 | 632.3279 | 672.981 | 714.9051 | 758.2408 | 815.3334 | 861.9422 | 919.1432 | 969.6766 | 1022.4385 | 1077.6193 | 1135.4202 | 1196.0539 | 1259.7454 | 1326.7332 | 1397.2698 | 1471.6233
Debt Interest | 224.496 | 240.1698 | 255.5966 | 270.8436 | 285.9787 | 301.071 | 316.1907 | 331.4096 | 355.367 | 370.7473 | 392.574 | 408.5012 | 424.918 | 441.9106 | 459.569 | 477.9866 | 497.2614 | 517.4955 | 538.7962 | 561.2763
Tax | 150.5651 | 161.0772 | 171.4237 | 181.6496 | 191.8004 | 201.9225 | 212.063 | 222.27 | 238.3377 | 248.653 | 263.2918 | 273.9738 | 284.9843 | 296.3809 | 308.224 | 320.5764 | 333.5036 | 347.0742 | 361.3602 | 376.4372
O&M | 797.6556 | 810.5487 | 824.0351 | 837.8554 | 852.0194 | 866.5373 | 881.4197 | 896.7993 | 921.3324 | 941.6552 | 950.7964 | 967.5427 | 982.6356 | 1006.3314 | 1024.079 | 1042.2915 | 1062.2964 | 1076.3829 | 1100.7874 | 1117.4206
Fuel and Purchased Power | 408.7404 | 429.907 | 412.4943 | 396.7879 | 416.8059 | 438.1178 | 457.6313 | 487.2171 | 496.1842 | 516.6518 | 538.9751 | 562.709 | 586.5963 | 599.5937 | 617.6827 | 634.3306 | 649.0982 | 673.4763 | 685.9442 | 706.3235
Average All-In Rate (¢/kWh) | 12.3029 | 12.8917 | 13.2894 | 13.6958 | 14.2789 | 14.8713 | 15.4597 | 16.1041 | 16.9062 | 17.5407 | 18.2877 | 18.9405 | 19.6011 | 20.268 | 20.9504 | 21.6501 | 22.3738 | 23.1419 | 23.9323 | 24.7558

## Slide 5: How do we represent EV impacts on utility sales?
Chart: EV impact on retail electricity sales (% of annual utility retail sales)
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
Low EV penetration | 0.0013994 | 0.0020202 | 0.0026366 | 0.0032486 | 0.003856 | 0.0044592 | 0.0050579 | 0.0056523 | 0.0062424 | 0.0068282 | 0.0074104 | 0.0081677 | 0.0089194 | 0.0096653 | 0.010406 | 0.01114 | 0.011869 | 0.012593 | 0.013311 | 0.014024
High EV penetration | 0.0014068 | 0.0045828 | 0.0077199 | 0.010819 | 0.01388 | 0.016904 | 0.019891 | 0.022842 | 0.025758 | 0.02864 | 0.031487 | 0.038442 | 0.045256 | 0.051935 | 0.058481 | 0.064899 | 0.071191 | 0.077362 | 0.083415 | 0.089353
High VMT penetration | 0.0023541 | 0.0076526 | 0.012864 | 0.01799 | 0.023033 | 0.027994 | 0.032876 | 0.03768 | 0.042407 | 0.047061 | 0.051642 | 0.06276 | 0.073555 | 0.084042 | 0.094233 | 0.10414 | 0.11377 | 0.12315 | 0.13227 | 0.14115
High VMT
(~14.0% increase 2040 retail sales)
High EV penetration (~9.0% increase in 2040 retail sales)
Low EV penetration (~1.5% increase in 2040 retail sales)

## Slide 6: How do we characterize EV impacts on utility generation and supply costs?
Generation capital, operations and maintenance (O&M), and FPP costs are modeled endogenously in FINDER using a built-in capacity expansion and dispatch logic.
Utility hourly load adjusted for incremental EVs
Hourly forecasts transformed into energy requirements by time period
Contributions of variable renewable energy and hour-to-hour ramp rates determined
Forward-looking capacity expansion that minimizes portfolio investment and operating costs
Weekly and hourly generation dispatch that minimized operating costs

## Slide 7: How do we characterize EV impacts on utility distribution and program costs?
Distribution CapEx Costs
Expert-elicited probability of feeder upgrades and costs driven by EV impacts on coincident peak and non-coincident peak
EV Charging Infrastructure Costs
EV Program Costs
Regulatory filing data to inform ratepayer-funded EVSE and control costs, as well as caps on program size
Regulatory filing data to inform ratepayer-funded EV program implementation and administrative costs, as well as caps on program size
Exogenous characterization

## Slide 8: Financial metrics
Earnings
Revenues - Costs
Quantifies future utility earnings opportunities
All-in Average Retail Rate
Revenues / Sales
Quantifies total rate impacts across all utility ratepayers
Metric
Calculation
Representation
All financial metrics are discounted over 20 years assuming a 7% nominal rate for utility earnings (representing average utility weighted average cost of capital) and a 5% nominal rate for average all-in retail rates and costs per EV.
Annual Cost per EV
Costs / EVs
Quantifies average incremental annual utility cost impact of integrating EVs (inclusive of utility generation, distribution, EV program, and charging control costs)

## Slide 9: What are the financial impacts of EVs under High Peak Impact charging? Comparison point: Utility without any incremental EV deployment

## Slide 10: EVs generally increase shareholder earnings and retail rates remain roughly unchanged
Chart: Change in financial metric compared to No EV (%)
| Low EV penetration | High EV penetration
Avg retail rates (20-yr NPV) | 0.0053492 | -0.0013145
Earnings (20-yr NPV) | 0.021601 | 0.047453

## Slide 11: Rate impacts are driven by timing of infrastructure investments and increase in sales
Chart: Change in 5-year average nominal retail rate compared to No EV (%)
| Low EV penetration | High EV penetration
2025 | 0.001858 | 0.016096
2030 | 0.0027799 | 0.0098901
2035 | 0.011792 | -0.0067964
2040 | 0.0052767 | -0.02938

## Slide 12: How does a Low Peak Impact charging strategy affect financial impacts, and how robust are results to different deployment assumptions? Comparison point: Utility with incremental EVs deployed with High Peak Impact charging

## Slide 13: Low Peak Impact charging reduces rates and earnings
Chart: Change in financial metric compared to High Peak Impact charging (%)
| Low EV penetration | High EV penetration
Avg retail rates (20-yr NPV) | -0.008455 | -0.0104
Earnings (20-yr NPV) | -0.018997 | -0.024038

## Slide 14: Financial impacts of Low Peak Impact charging are directionally consistent across sensitivities
Chart: 
| Earnings (20-yr NPV)
High | -0.0030077
Sensitivity range | -0.021486
Low EV penetration | -0.018997 | -0.018997
High EV penetration | -0.024038 | -0.024038
Chart: Change in financial metric compared to High Peak Impact charging (%)
| Avg retail rates (20-yr NPV)
High | -0.0016085
Sensitivity range | -0.0093575
Low EV penetration | -0.008455 | -0.008455
High EV penetration | -0.0104 | -0.0104

## Slide 15: Managed charging strategies reduce the incremental annual cost of integrating EVs by ~38-62%
Chart: Annual $/EV (20-yr discount-weighted)
| High Peak Impact | Low Peak Impact | High Peak Impact | Low Peak Impact
 | 615.6068 | 231.7516 | 471.2526 | 292.616

## Slide 16: Key findings and discussion
Ratepayers are almost always better off and more so if EVs are deployed with managed charging strategies.
Compared to a future without EVs, shareholder are also better off, but managed charging erodes some of the incremental earnings.
A forward-looking and long-term perspective is necessary to make large initial utility infrastructure investments that enable greater EV deployment and result in later rate decreases.
Impacts are overall quite small on a total utility basis; but, they could be more significant for particular customer classes depending on cost allocation and cost recovery, which were not explored in the study.
To trigger managed behavior we model requires dynamic infrastructure planning process and/or flexible managed charging strategy to reflect how the utility load shape evolves inclusive EV load (e.g., EV TOU periods will change from overnight to middle-of-day as coincident peak EV load impacts build).

## Slide 17: Future research opportunities
Assume different EV penetration levels and adoption rates.
Explore additional charging strategies and profiles, utility characterizations, and customer-class impacts.
Model medium-duty and heavy-duty EVs (MDVs and HDVs).
Incorporate a more detailed distribution cost model.
Model EV-specific rate designs and quantify cost shifts between EV owners and non-EV owners.

## Slide 18
Contacts
  Andrew Satchwell | ASatchwell@lbl.gov
For more information
  Download publications from the Electricity Markets & Policy: https://emp.lbl.gov/publications
  Sign up for our email list: https://emp.lbl.gov/mailing-list
  Follow the Electricity Markets & Policy on Twitter: @BerkeleyLabEMP
Acknowledgements
  This work was funded by the U.S. Department of Energy (DOE) Office of Energy Efficiency and Renewable Energy (EERE) Strategic Analysis Team (SA) under Contract No. DE-AC02-05CH11231. We would like to especially thank Ookie Ma and Kara Podkaminer (DOE) for their support of this work. For reviewing the study and providing valuable feedback, we thank Michelle Levinson (World Resources Institute), Galen Barbose (Berkeley Lab), and Kara Podkaminer, Noel Crisostomo, and Paul Spitsen (DOE).
  The views and opinions of authors expressed herein do not necessarily state or reflect those of the United States Government or any agency thereof, or The Regents of the University of California.

## Slide 19: Berkeley Lab’s FINDER model
The FINDER model is a pro-forma financial model of changes in utility costs and revenues with the addition of DERs.
Model outputs include shareholder metrics (achieved return-on-equity (ROE) and earnings) and ratepayer metrics (average retail rates and bills).
The FINDER model has been developed over more than 14 years and used to support foundational research and state technical assistance in seven states and two regions.
For more information on the FINDER model and related publications, see: https://emp.lbl.gov/projects/finder-model

## Slide 20: Distribution CapEx
Problem: estimate physical and monetary distribution system expansion based on EV load
Existing solutions are based on a simple $/EV value with very little empirical support
Our solution:
  Leverage expert elicitation for cumulative probability of distribution system upgrades produced by CalETC
  Convolve with normal distribution for EV load distribution across feeder. Use CP load for substation and primary system, and NCP load for secondary system
  Determine the share of feeders requiring an upgrade
  Monetize based on CalETC’s expert elicitation using high/low ranges given the uncertainty; scale up to the size of the representative utility

## Slide 21: Utility EV charging infrastructure and program costs
Scenario Element | Low value | Medium value | High value | Managed charging adder | Accounting treatment
L1 charger cost ($/L1 charger) | $0 | $0 | $0 | $0 | N/A
L2 charger cost ($/L2 charger) | $1,529 | $7,143 | $15,829 | $1,200 per residential charger and $2,200 per workplace charger | Capitalize
DCFC charger cost ($/DCFC charger) | $38,320 | $66,250 | $149,753 | $0 | Capitalize
Annual program cost | $70,800 | $619,500 | $2,494,800 | $0 | Expense
Program cap | 1/3 total charger deployment | 1/6 total charger deployment | 1/12 total charger deployment | N/A | N/A